## Slide 1: Exploiting Amorphous Data Parallelism with the Explicit-Parallel-Call Architecture
Ji Kim
Computer Systems Laboratory
Cornell University
10/08/2014

## Slide 2: Present: Coarse-Grain Heterogeneity
Technology challenges are forcing new abstractions
Trend toward coarse-grain heterogeneous architectures (Intel Haswell, AMD Kabini, NVIDIA Tegra, etc.)
Motivation FG-SIMT HWWL XPC Methodology Roadmap
Notes: A lot of serious technology challenges including power constraints and end of traditional CMOS scaling
Computer architects turning to new abstractions to achieve higher performance and energy efficiency
Requires innovation across HW/SW boundaries
Examples in industry with coarse-grain heterogeneity, usually a set of general-purpose cores with a data-parallel accelerator

## Slide 3: Present: Coarse-Grain Heterogeneity
AMD Heterogeneous System Architecture (HSA) aims to unify heterogeneous tiles with an intermediate SW layer
  OpenCL -> Virtual ISA -> tile-specific ISA
  Unified virtual memory to simplify inter-tile data transfer
  Runtime for optimal scheduling
Coarse-grain tasks (i.e., kernel launch)
Exposes traditional data parallelism
Heterogeneous System Architecture: A Technical Review. AMD Whitepaper, 2012.
http://www.hsafoundation.com/publications/
Motivation FG-SIMT HWWL XPC Methodology Roadmap
Notes: AMD’s HSA is one approach to unifying heterogeneous architectures
Uses an intermediate virtualization layer in SW to map kernels to various microarchitectures
Essentially a clean wrapper for existing microarchitectures with their own ISAs
Reduce inter-tile communication latency with unified virtual memory
Fine-grain function calls may be preferable with applications where most of the work is dynamically generated, allowing for more flexible, adaptive load balancing
Find more opportunities for HW acceleration of amorphous data parallelism within tiles

## Slide 4: Present: Traditional Data Parallelism
vvadd( int* dest, int* src0, int* src1, int size ):
for i in range( size ):
dest[i] = src0[i] + src1[i]
Motivation FG-SIMT HWWL XPC Methodology Roadmap
Notes: Commonly exploited on SIMD or SIMT
Same task operates on elements of independent input and output arrays
Note that both the control flow and data structure are highly regular

## Slide 5: Future: Amorphous Data Parallelism
bfs( Node* nodes, Worklist* wl ):
while wl not empty:
index = wl->pull()
my_node = node[index]
for all neighbors of my_node:
if my_node.dist + 1 < neighbor.dist:
neighbor.dist = my_node.dist + 1
wl->push( neighbor.index )
K. Pingali et al. The Tao of Parallelism in Algorithms. PLDI 2011.
Motivation FG-SIMT HWWL XPC Methodology Roadmap
Notes: A more generalized form of data parallelism first defined in Pingali paper
Extends traditional data parallelism with relaxed constraints
Elements can belong to multiple tasks, requiring some conflict resolution
Output graph is a modified version of the input graph
Tasks are dynamically generated by other tasks

## Slide 6: Traditional vs. Amorphous Data Parallelism
Characteristic | Traditional | Amorphous
Control Flow | Regular | Data-Dependent
Data Structure | Regular | Irregular
Task Inputs/Outputs | Disjoint | Overlapped
Task Generation | Static | Dynamic
Motivation FG-SIMT HWWL XPC Methodology Roadmap
Notes: Summary of differences between traditional and amorphous data parallelism
ADP extends TDP (i.e., superset)
Can we capture amorphous data parallelism, so that we can ubiquitously exploit this parallelism on any microarchitecture?
Ji: need a more explicit way of explaining how parallel function calls better expose ADP (is it more about the parallel primitives we provide?)

## Slide 7: Future: Fine-Grain Heterogeneity
Less parallelization overhead (i.e., kernel launches)
No need to commit to parallelizing for one microarchitecture
Better suited for amorphous data parallelism
  Improved load balancing for dynamically generated work
  Flexible adaptive execution for changing parallelism
Motivation FG-SIMT HWWL XPC Methodology Roadmap
Notes: Future will trend toward fine-grain heterogeneous architectures
Intermingling of fine-grain tiles (converging of CPU and GPU)
Fine-grain allows for:
  Less parallelization overhead
  No need to know whether programming for CPU or GPU
  Better for exploiting ADP
ADP has unpredictable, changing parallelism for a single workload
ADP has dynamically generated work which would work better as fine-grain tasks for load balancing

## Slide 8: Explicit-Parallel-Call Architecture
FG-SIMT. Kim et al.
ISCA 2013.
XLOOPS. Srinath et al.
MICRO 2014.
HWWL. Kim et al.
MICRO 2014.
Motivation FG-SIMT HWWL XPC Methodology Roadmap
Notes: At a high-level, the XPC architecture can be broken down into:
  XPC programming framework, which allows users to expose opportunities for fine-grain parallel tasks
  XPC runtime, which facilitates adaptive scheduling of fine-grain parallel tasks
  XPC tiles (TCL, LCL, CMC, etc.), which are specialized for efficiently exploiting fine-grain parallel tasks with varying levels of amorphous data parallelism
We will draw on previous works as inspiration in designing pieces of the XPC architecture

## Slide 9: Explicit-Parallel-Call Design Space
 | Software | Hardware
Exposing opportunities for fine-grain parallel tasks | Parallel function calls (tasks stored in memory) | Task cache
Scheduling fine-grain parallel tasks | Adaptive runtime | Work distribution network
Executing fine-grain parallel tasks | Application running on native multicore | Amorphous data parallel accelerators (XPC tiles)
Explore different permutations of SW/HW techniques
Notes: Can describe XPC with three key facets of fine-grain parallel tasks
Mix and match SW and HW techniques for three key facets of XPC architecture
Baseline uses all SW techniques by default
Most interesting and compelling permutation is using HW acceleration for all facets of XPC
HW acceleration for ADP
  Conflict detection for overlapped tasks (speculative_for, atomic_for)
  Dynamic task generation (task cache?)

## Slide 10: Overview
Fine-Grain SIMT
Fine-Grain Hardware Worklists
Explicit-Parallel-Call Architecture
Methodology

## Slide 11: Fine-Grain SIMT at a Glance
Tightly integrated data-parallel accelerator
Focus on fine-grain parallelization and area efficiency
Exploit traditional data parallelism
J. Kim et al. Microarchitectural Mechanisms for Exploiting Value Structure in SIMT Architectures. ISCA 2013.
Notes: Best suited for TDP (can still handle ADP, but loses efficiency)
Groups of threads execute in lock-step across lanes and memory accesses are coalesced when possible (weak to control and memory-access irregularity)
FG-SIMT has fine-grain thread scheduling on tightly coupled CPU + SIMT unit
FG-SIMT focuses on exploiting intra-warp parallelism for area efficiency (instead of multithreading)
FG-SIMT also allows us to exploit value structure to further accelerate TDP by using compact affine execution
  Looking at TDP figure, we can see missed opportunities for eliminating redundancy if elements are uniform

## Slide 12: Identifying Value Structure
__global__ void
vsadd( int y[], int a ) {
int idx = // get thread index
y[idx] = y[idx] + a;
if ( y[idx] > THRESHOLD )
y[idx] = Y_MAX_VALUE;
}
Value Structure occurs when the same operation uses values across threads which can be represented as a compact function.
vsadd:
ld.sh R_a, M[A]
ld.sh R_ybase, M[Y]
add R_yptr, R_ybase, IDX
load R_y, M[R_yptr]
add R_y, R_y, R_a
store R_y, M[R_yptr]
branch R_y, THRESHOLD
imm R_max, Y_MAX_VALUE
store R_max, M[R_yptr]
stop
R_a
R_ybase
R_ybase
R_a
R_max
R_max
THRESHOLD
Y_MAX_VALUE
R_yptr
IDX
R_yptr
R_yptr
R_yptr
Affine Value Structure:
44
2
32
40
3
2
2
2
32
32
32
40
40
40
0
1
2
32
36
40
127
19
89
8
8/27
Notes: In order to understand what value structure is, we’ll be using our ongoing example of vector-scalar add shown here on the left. The pseudo-assembly this translates to is shown here on the right.
In the C code, each thread reads its thread index, which is then used to index a unique element of the array, we add a scalar value to this element and write it back to the array. If the result is greater than a threshold, we instead write the saturated maximum value to the array.
In the assembly, we start by loading the scalar value “a” and the address of the y array. The thread index is added to the base address to obtain the address of the element in the y array that each thread wants to access. We load from that address, add the scalar “a” value, then store it back into the array. This branch condition catches the case when the result is greater than the threshold, in which case we store the maximum value to the array.
As a reminder, we define value structure as occurring when… (read the rest)
Let’s see if we can find some examples of value structure in this example.
First, we can identify some variables that are the same for all threads: the scalar “a” value, the threshold and the maximum value circled here are some examples. In the assembly, these correspond to these registers. The picture on the bottom shows a register file layout of four worker threads. You can see that the same values are redundantly stored across all threads.
We can also identify some values which increase by a set amount for increasing thread indices. An obvious example of this is the thread index itself which increments by one for each succeeding thread. Adding the thread index to the base address maintains this pattern which we can see on the bottom*.
This particular type of value structure is called “affine value structure”, and adheres to the formula shown here, where “b” is the base, “i” is the thread index, and “s” is the stride. For example, the affine value in R_yptr has a base of 16 and a stride of 1. We can compactly encode affine values as a base and stride pair. Note that the value structure seen in R_a and R_ybase are a special case of affine value structure where the stride is 0. For example, the affine value in R_a has a base of 2 and a stride of 0. We call this special case “uniform value structure”.
All other registers which do not have any type of structure, such as R_y, are called generic values. We can see that the the register values for R_y have no apparent pattern to them.
*Technically needs to be multiplied by 4, but skip for simplicity…

## Slide 13: FG-SIMT Example Execution
18/27
Notes: Affine arithmetic on operands that have affine values
Affine memory operations on loads to affine addresses (within limits)
Affine branches on uniform conditions
Affine execution allows us to eliminate redundancy and compactly execute instructions on the CP once instead of spread out across SIMT lanes
Note we cannot exploit value structure after divergence because we would need different states of the ASRF for different fragments
  Performance overhead when overwriting affine register after divergence (make value available to all fragments)

## Slide 14
19/27
Notes: Improve both performance and energy efficiency

## Slide 15: Affine Expansion
20/27
Cannot exploit value structure after divergence
  Would require multiple states of affine registers
  Best case with traditional data parallelism
Overhead from overwriting affine register after divergence
5
6

## Slide 16: FG-SIMT Performance

## Slide 17: FG-SIMT Energy vs. Performance
viterbi
  54% saved within register file
  29% saved within functional units
  34% saved within memory system
strsearch
  115 to 130 uJ per task
  89% of 15 uJ due to expansion units
26/27
Baseline
Notes: Here is a scatter plot of energy vs. performance for all our benchmarks. Results are only shown for FG-SIMT with all affine mechanisms enabled, normalized to the baseline FG-SIMT design shown by the red dot. Most of our benchmarks are in the lower right hand side of this point, meaning they achieve greater energy-efficiency and performance, with energy-efficiency improving up to 30% in the best case. Overall, compact affine execution reduces the amount of required to complete the same task. In one of the best cases, viterbi, we saw energy savings of 54% in the combined register files from using the efficient ASRF instead of the large SIMT register files, 29% in the combined functional units from eliminating redundant computation with affine execution, and 34% in the memory system from more efficient accesses due to affine memory operations.
The benchmarks which have worse energy-efficiency still manage to do slightly better in terms of performance compared to the baseline. Much of this overhead is due to the divergent nature of these benchmarks which trigger affine destination expansions. For example, in the worst case, strsearch, energy consumption increases from 115 to 130 uJ, an increase of 12%. 89% of this 15 uJ increase is attributed to the expansion units in the SIMT lanes, corroborating this theory.
Although the apps that do not improve do not hurt performance, they do incur a noticeable energy overhead. This is due to the overhead of affine destination expansion after divergence and relatively small application vector lengths (in the case of rsort). For future work, we are looking into improving opportunities for affine execution after divergence to eliminate this overhead, as well as exploring FG-SIMT as an alternative integrated data-parallel accelerator in general.

## Slide 18: Overview
Fine-Grain SIMT
Fine-Grain Hardware Worklists
Explicit-Parallel-Call Architecture
Methodology

## Slide 19: Fine-Grain Hardware Worklist at a Glance
Accelerate irregular algorithms on GPGPUs
Reduce memory contention and improve load balancing
Exploit irregular amorphous data parallelism
J. Kim et al. Accelerating Irregular Algorithms on GPGPUs with Fine-Grain Hardware Worklists. MICRO 2014.

## Slide 20: Topology-Driven Approach
def topo_driven:
idx = get_tid()
my_node = nodes[idx]
if check( my_node ):
compute( my_node )
*done_ptr = false;
def main:
done = false; while not done:
done = true
topo_driven<<<N>>>( nodes, &done )
Data-Driven Approach
Determine work with thread index
Visits all nodes (even inactive)
# threads spawned = # nodes
Limited dynamic load balancing
Less work efficient
Determine work with worklist
Visits only active nodes
# threads spawned = # HW threads
No dynamic load balancing
High memory contention
def data_driven:
for wid in range( start, end ):
idx = pullwl.pull( wid )
my_node = nodes[idx]
compute( my_node )
for all neighbors of my_node:
if check( neighbor ):
pushwl.push( neighbor.idx )
def main:
init_wl<<<N>>>( nodes, pullwl )
while not pullwl.empty():
data_driven<<<M>>>( nodes, wl )
swap( pullwl, pushwl )
Notes: Topology-driven: less work efficient, but simpler (no issues with memory contention)
Data-driven: more work efficient, but issues with memory contention due to shared worklist
Both variants have issues with load balancing
Data-driven variant usually written with double-buffering to eliminate AMOs on pulls
  Single-buffering has better load balancing, but memory contention makes it unviable

## Slide 21: GPU Results with Optimizations
Data-driven outperforms topology-driven with optimizations
Experiments on real GPU with hand-optimized benchmarks
Focus on addressing weaknesses of data-driven approach
Notes: Add list of optimizations?

## Slide 22: HWWL Microarchitecture
Interact with HWWL using pull/push instructions
On empty pulls, force thread to wait if more work in system
HWWL interfaces with GPGPU pipeline with special units
  Arbitration required when accessing GPGPU regfile
Instruction | Description
wlpull | Pulls work ID from HWWL. If bank is empty: return WAIT if work in other banks, otherwise return DONE.
wlpush | Pushes work ID to HWWL, throws exception if overflow buffer is full.
Notes: Pulls move work IDs from HWWL to GRF
Pushes moves work from GRF to HWWL

## Slide 23: HWWL Microarchitecture
Notes: Distributed per-lane HWWL banks to avoid memory accesses when interacting with worklist (1rw SRAMs)
WRU aggregates meta-data regarding bank occupancy to determine how to distribute work
  Prioritize intra-core before inter-core work redistribution
  ICRN facilitates inter-core work redistribution
HVU handles virtualization of work that does not fit in the HWWL to an overflow buffer in memory

## Slide 24: HWWL Work Redistribution
Threshold
  Banks with work over threshold donate to those with work below threshold
  Simple, scalable, minor load balancing
Local Sorting
  Each core sorts banks by amount of work, banks with most work donate to those with least work
  Requires sorting network, still scalable, improved load balancing
Global Sorting
  Monolithic WRU sorts all banks in system, only globally greedy banks are eligible to donate work to globally needy banks
  Increased HW complexity, not scalable, provides more info to WRU
Notes: All interval-based schemes (mention on-demand?)
Redistro schemes tradeoff HW complexity for better load balancing
lsorting: even needy banks can donate to other needy banks (helps case where all banks are below threshold)
gsorting: prevents banks which are globally greedy from getting more work because it is locally needy
Top half is greedy, lower half is needy
If there are more greedy banks than needy banks in a core, that core sends work to a core with more needy banks than greedy banks via the ICRN

## Slide 25: HWWL Idealized Performance

## Slide 26: HWWL Work Redistribution Comparison

## Slide 27: Realistic HWWL Performance
Realistic HWWL design with 512 entries per core, local-sorting work redistribution, and interval-based virtualization
Roughly additional area overhead of 2.5% of GPGPU regfile

## Slide 28: Overview
Fine-Grain SIMT
Fine-Grain Hardware Worklists
Explicit-Parallel-Call Architecture
Methodology

## Slide 29: Explicit-Parallel-Call Design Space
 | Software | Hardware
Exposing opportunities for fine-grain parallel tasks | Parallel function calls (tasks stored in memory) | Task cache
Scheduling fine-grain parallel tasks | Adaptive runtime | Work distribution network
Executing fine-grain parallel tasks | Application running on native multicore | Amorphous data parallel accelerators (XPC tiles)

## Slide 30: Exposing Parallel Tasks: Programming API
13/21
Highly productive parallel programming API
Algorithm-centric approach with a focus on exposing amorphous data parallelism
Four parallel constructs
  spawn
  parallel_for
  atomic_for
  speculative_for

## Slide 31: Exposing Parallel Tasks: Programming API
14/21
spawn( index, function )
  Recursive divide-and-conquer
void bfs( Node* nodes ) {
ppp<xpc>::spawn( start, func = [&] ( int idx ) {
Node my_node = node[idx];
for ( i = 0; i < my_node.num_neighbors; i++ ) {
Node neighbor = my_node.neighbors[idx];
if ( my_node.dist + 1 < neighbor.dist ) {
neighbor.dist = my_node.dist + 1;
xpc::spawn( neighbor.idx, func );
}
}
});
}

## Slide 32: Exposing Parallel Tasks: Programming API
15/21
parallel_for( num_calls, function )
  Parallelize across loop iterations (i.e., tasks)
void bfs( Node* nodes ) {
Worklist inwl, outwl;
inwl.push( start );
while ( inwl.size() > 0 ) {
ppp<xpc>::parallel_for( inwl.size(), [&] ( int idx ) {
Node my_node = node[inwl.pull(idx)];
for ( i = 0; i < my_node.num_neighbors; i++ ) {
Node neighbor = my_node.neighbors[i];
if ( my_node.dist + 1 < neighbor.dist ) {
neighbor.dist = my_node.dist + 1;
outwl.push( neighbor.idx );
}
}
});
swap( inwl, outwl );
}
}

## Slide 33: Exposing Parallel Tasks: Programming API
16/21
atomic_for( num_calls, function )
  Similar to parallel_for except tasks are guaranteed atomicity
void mm( Edge* out_edges, Edge* in_edges ) {
bool matched[num_nodes];
ppp<xpc>::atomic_for( num_edges, [&] ( int idx ) {
int u = in_edges[idx].u;
int v = in_edges[idx].v;
if ( !matched[u] && !matched[v] ) {
matched[u] = matched[v] = true;
out_edges[idx] = in_edges[idx];
}
});
}
Notes: Fine subset of edges which span all nodes exactly once

## Slide 34: Exposing Parallel Tasks: Programming API
17/21
speculative_for( num_calls, reserve_func, commit_func )
  Split tasks into reserve and commit phases to ensure atomicity
void mm( Edge* out_edges, Edge* in_edges ) {
ppp<xpc>::speculative_for( num_edges,
reserve_func = [&] ( int idx ) {
int u = in_edges[idx].u;
int v = in_edges[idx].v;
if ( matched[u] || matched[v] ) return false;
reserves[u] = reserves[v] = idx;
return true;
},
commit_func = [&] ( int idx ) {
if ( reserves[u] == reserves[v] == idx ) {
matched[u] = matched[v] = true;
out_edges[idx] = in_edges[idx];
return true;
}
return false;
}
);
}

## Slide 35: Exposing Parallel Tasks: XPC ISA
9/21
Instruction | Description
pcall n, func | Make n instances of function available for parallel execution (serial execution is valid)
psync | Wait for all child parallel calls to complete
pret | Return from parallel call (uses different return address from standard function call)
Notes: * Pull model where functions may or may not be executed in parallel, as opposed to push model we are more used to like bthreads where we actively push tasks onto threads

## Slide 36: Explicit-Parallel-Call Design Space
 | Software | Hardware
Exposing opportunities for fine-grain parallel tasks | Parallel function calls (tasks stored in memory) | Task cache
Scheduling fine-grain parallel tasks | Adaptive runtime | Work distribution network
Executing fine-grain parallel tasks | Application running on native multicore | Amorphous data parallel accelerators (XPC tiles)

## Slide 37: Scheduling Parallel Tasks: Adaptive Runtime
18/21
Software-based adaptive execution
  Always running on idle tiles to facilitate work stealing
  Ideal if lightweight to minimize software overhead
Collect heuristics to determine when/where to schedule tasks
  Raw performance (compare to threshold or history)
  Control irregularity (e.g., number of warp fragments)
  Memory-access irregularity (e.g., number of uncoalesced accesses)
Hardware support for runtime?
  Inter-tile task distribution unit exposed to runtime (not to user)
  Hardware performance counters for heuristics

## Slide 38: Explicit-Parallel-Call Design Space
 | Software | Hardware
Exposing opportunities for fine-grain parallel tasks | Parallel function calls (tasks stored in memory) | Task cache
Scheduling fine-grain parallel tasks | Adaptive runtime | Work distribution network
Executing fine-grain parallel tasks | Application running on native multicore | Amorphous data parallel accelerators (XPC tiles)

## Slide 39: Executing Tasks: Tightly-Coupled Lanes (TCL)
10/21
High performance and energy efficiency for traditional data parallelism
Amortized front-end, lock-step execution
Affine execution accelerates value structure
Suffers with control and memory-access irregularity
Notes: Traditional execution is difficult
Memory communication (vs. registers)
No support for nested parallelism

## Slide 40: Executing Tasks: Loosely-Coupled Lanes (LCL)
11/21
Better tolerance for irregular amorphous data parallelism
Decoupled control flow between lanes using instruction buffers
More lightweight lanes with shared ‘expensive’ FUs
Good middle-ground specialization before resorting to general-purpose
Notes: Dynamic bound, communicate back to lane manager?
Still depends on some level of regularity and control flow divergence constrained by size of instruction buffer

## Slide 41: Executing Tasks: Cooperative Multicore (CMC)
12/21
General-purpose, capable of handling highly irregular amorphous data parallelism
No significant performance or energy benefits regular control and memory-access
Internal task distribution unit
Default tile to collect heuristics for migration?

## Slide 42: Single-Tile Multiple-Accelerator Design
19/21
Reasonable design point for exploring XPC
Single tile with three sub-tiles: scalar CP, TCL, LCL
CP responsible for generating work which can be stolen by TCL or LCL accelerators
Shared memory system minimizes migration overhead

## Slide 43: Overview
Fine-Grain SIMT
Fine-Grain Hardware Worklists
Explicit-Parallel-Call Architecture
Methodology

## Slide 44: Methodology
21/21
GEM5 driver with verilated RTL
PyMTL cycle-level models
Verify cycle time, area, and energy with ASIC flow
Chip tapeout

## Slide 45: Roadmap
XPC Single-Tile Multi-Accelerator Design
  Submit to ISCA 2015 (June 2015)
Chip Tapeout for XPC Subset
  Spring 2015 – Fall 2015
Industry Internship
  Summer 2015
Exploring Multi-Tile XPC Architecture
  Fall 2015 – Spring 2016

## Slide 46: Backup Slides
Fine-Grain SIMT
Fine-Grain Hardware Worklists
Explicit-Parallel-Call Architecture
Methodology

## Slide 47: Data-Driven Optimizations
def data_driven_2buf:
start = tid * N/M
end = tid + N/M
for wid in range( start, end ):
idx = pullwl.pull( wid )
my_node = nodes[idx]
compute( my_node )
for all neighbors of my_node:
if check( neighbor ):
pushwl.push( neighbor.idx )
def main:
init_wl<<<N>>>( nodes, pullwl )
while not pullwl.empty():
data_driven<<<M>>>( nodes,
pullwl, pushwl )
swap( pullwl, pushwl )
Double-Buffering
  Eliminate memory contention on pulls
  Cannot overlap super-steps anymore!
Work Chunking
  Amortize push over multiple elements
  Reduce memory contention on pushes
Work Donating
  Donate excess work to other threads in the same block via GPU shared mem
  Helps load balancing
Variable Kernel Configuration
  Adjust number of threads spawned if super-step has less work than HW threads
  Helps work efficiency
def data_driven:
while not wl.empty():
idx = wl.pull()
my_node = nodes[idx]
compute( my_node )
for all neighbors of my_node:
if check( neighbor ):
wl.push( neighbor.idx )
def main:
init_wl<<<N>>>( nodes, wl )
data_driven<<<M>>>( nodes, wl )
Notes: Even though data-driven is more algorithmically efficient, the high memory contention due to accessing a shared worklist makes it inferior to topology-driven without signficant optimizations.

## Slide 48: Explicit-Parallel-Call Architecture
Expose amorphous data parallelism as parallel function calls
Parallel calls can be nested for dynamic task generation
Pull-based model means creating opportunities for parallelism
Motivation FG-SIMT HWWL XPC Methodology Roadmap
Notes: Pull-based model (i.e., work-stealing) means we can always fall back to executing serially if resources are busy or non-existent
SW runtime dynamically handles which function calls are parallelized
NVIDIA dynamic parallelism allow nested kernel launches too, but is a coarse-grain approach and only for GPGPUs (not heterogeneous)

## Slide 49: FG-SIMT Example Execution
12/27
Notes: In order to understand how FG-SIMT works, we’ll look at an example execution of the vector-scalar example code. Shown here is a cartoon of the FG-SIMT microarchitecture. The control processor, which is a simple 5-stage MIPS core on its own, acts as the front-end of the system and issues instructions from the kernel to the SIMT issue unit (SIU), the SIU schedules micro-instructions to all of the SIMT lanes which contain the SIMT register file, and both integer and floating point functional units. The SIMT memory unit manages all memory transactions generated by the SIMT lanes and handles coalescing.

## Slide 50: Exploiting Value Structure
vsadd:
ld.sh R_a, M[A]
ld.sh R_ybase, M[Y]
add R_yptr, R_ybase, IDX
load R_y, M[R_yptr]
add R_y, R_y, R_a
store R_y, M[R_yptr]
branch R_y, THRESHOLD
imm R_max, Y_MAX_VALUE
store R_max, M[R_yptr]
stop
15/27
Affine arithmetic
vsadd:
ld.sh R_a, M[A]
ld.sh R_ybase, M[Y]
add R_yptr, R_ybase, IDX
load R_y, M[R_yptr]
add R_y, R_y, R_a
store R_y, M[R_yptr]
branch R_y, THRESHOLD
imm R_max, Y_MAX_VALUE
store R_max, M[R_yptr]
stop
addiu
lui
addu
subu
sll/sllv
srl/srlv
sra/srav
mul
Affine arithmetic
Affine memory operations
vsadd:
ld.sh R_a, M[A]
ld.sh R_ybase, M[Y]
add R_yptr, R_ybase, IDX
load R_y, M[R_yptr]
add R_y, R_y, R_a
store R_y, M[R_yptr]
branch R_y, THRESHOLD
imm R_max, Y_MAX_VALUE
store R_max, M[R_yptr]
stop
addiu
lui
addu
subu
sll/sllv
srl/srlv
sra/srav
mul
lw/lh/lb
sw/sh/sb
Affine arithmetic
Affine memory operations
Affine branches
vsadd:
ld.sh R_a, M[A]
ld.sh R_ybase, M[Y]
add R_yptr, R_ybase, IDX
load R_y, M[R_yptr]
add R_y, R_y, R_a
store R_y, M[R_yptr]
branch R_y, THRESHOLD
imm R_max, Y_MAX_VALUE
store R_max, M[R_yptr]
stop
addiu
lui
addu
subu
sll/sllv
srl/srlv
sra/srav
mul
lw/lh/lb
sw/sh/sb
beq/bne
blez/bgez
bltz/bgtz
15/27
Eliminate redundancy to improve performance and energy efficiency
Notes: For each type of instruction we can exploit value structure for, I’ll be highlighting the instruction in red. Here, I’m going to start with the first two shared loads highlighted since we get these for free in the baseline as well.

## Slide 51: Tracking Value Structure
Store affine values in Affine SIMT Register File (ASRF)
ASRF encodes affine values as base and stride pair with uniform/affine tags
Registers are tagged as affine when:
  Shared loads (e.g., ld.param, ld.sh)
  Thread index (e.g., tid.x, IDX)
  Result of affine arithmetic
14/27
Notes: Affine values are stored in a special register file called the affine SIMT register file (ASRF). The ASRF encodes an affine value as a base and stride pair, and tags each entry as uniform or affine.
As I alluded to before, registers can be tagged as affine if it is the destination of a shared load, thread index, or affine arithmetic.
We can exploit value structure in arithmetic, control, and memory instructions.

## Slide 52: Nested Parallelism
21/21
Nested parallelism
  Interesting opportunities to more generically expose previously underutilized parallelism!
  Allow any level of nesting to produce generic fine-grain tasks that can map to any sub-tile (function pointer, context pointer, call count)
  Hardware support for nested parallelism on TCL? (LCL can handle)
    pcall instruction on TCL triggers push to special task buffer which lazily updates memory? Would not look like function call in TCL, no divergence